Use and attentions of the following device

1：Software instruction

To be shown as the figure

The area in red profile is the set for the following device control part. In the main page, “F5 Set parameter”——“F5 Set parameter”—— “Option of detect high”, choose “ Yes”, then choose “ Normally open contact”

2．Hardware instruction

To be shown as the figure

Item 1 is the rotary switch   Use: to fix the detecter

Item 2 is the detecter      Use: It is used to detect the tilt of processing material, and adjust the height, protect the cutting head.

Installation and adjustment: Install the detecter first, so that the nozzle can move in the round hole of the detecter’s bottom. The rotary detecter can move up and down and the height distance can be controlled by the rotary switch.

Note: The nozzle should be on the above of the round hole, not inside or through it. Or the cutting head will be hit and breaks the nozzle.